## Slide 1: Invest: safe-tee
by Madeleine Dwyer, Wen Fan, Ziye Hu, Yanting Liu,
Baiting Luo, Adam Platek, Kangning Wang and Yuheng Zhou

## Slide 2: Agenda
Introduction & Problem Statement
Customer Needs & Requirements
Performance Specifications
Risk assessment
Team Skills
Design Alternative
Concept Selection
Prototype Subsystem Design
Prototype Design
Comparison between
Prototype and Final Design
Testing
Complications
Production Ramp Up
Review & Reflect
Validation through
Customer Requirements
What We Learned
Conclusion
References

## Slide 3: Introduction
37.7 million people on average fall and require medical attention each year (12%)!
Displacement Fracture of Knee Joint
424,000 people die each year from fall-related injuries.
[24]
References: 52.

## Slide 4: Problem statement
2/3 of victims will fall a second time within 6 months
1/4 of elders who fall and fracture a hip will die within 6 months.
Target customer: elderly (65+), disabled, and therapy patients
Displacement Fracture of Hip Joint
[27]
References: 41.

## Slide 5: Customer Requirements
Safety
Maximum Weight Limit
Comfort
Suitable Size
Plate Location
stomach, shoulder, rib, heart, hip plates
Sufficient Catch Height
at least .91 meters
890 Newtons
Affordable & Fashionable
standard unisex sizes (cm) Medium - Chest (96-102), Waist - (81-84)
Suitable Weight
Max 89 Newtons
Temperature Moderation
At least 4 holes, >3 ventilation areas additional
Ease of Use
Number of Parts
10 max
Time to assemble
20 minutes max
Time to reassemble
5 minutes max
Time to put on
3 minutes max
Percent Shrinkage
assuming washable, less than 5%
Percent Dampness
0% water reaching sensors
Purchase cost
< $500 (subjective to change of cost analysis)
Maintenance cost
< $50 monthly
Color
Subjective
Shape
Subjective

## Slide 6: System Design Alternatives
Shoe Design
Backpack Design
Concept Score: 35.9
Concept Score: 36.9
Vest Design
Concept Score: 67

## Slide 7: Vest Design Alternatives
Spring Design
Airbag Design
Concept Score: 51.3
Concept Score: 49
Arm Design
Concept Score: 65
References: 3.

## Slide 8: Performance Specifications
Detecting：
Sensor Type: [LM393] PCB
Board Size : 310 x 170mm
Sensor Weight :13g
3-Axis Gyroscope & Accelerometer
Alarming：
Tone Generation Range： 1.5 ~ 2.5kHz
Dimensions ：12x10mm
Item Weight : 25g
Supporting：
Steel Arm
Arm:
56cm long
out diameter: 190 mm
inner diameter:158 mm
References: 2, 10, 11, 15, 17, 30, 38, 42, 45, 50.

## Slide 9: Risk Assessment
Risk | Causes | Root Cause | RPN | Risk Mitigation | New RPN | Who is in charge
Arms Breaking | Metal shears | Deployment of arms at an angle | 360 | Buzzer | 72 | Electrical Team
 |  | Exceeds force design limits | 360 | Various designs | 200 | Inflation Team
 | Joints break | Deployment at an angle | 630 | Buzzer | 126 | Electrical Team
 | Exceeds limits | Stairs | 270 | Cushion | 135 | Inflation Team
Kydex cracking | Heavy impact | Force exceeds design limits | 49 | Maintenance | 35 | Design Team
References: 25, 48.

## Slide 10: Risk Assessment
Risk | Causes | Root Cause | RPN | Risk Mitigation | New RPN | Who is in charge
Sensor not detecting | Sensor gets wet | Rain | 280 | Waterproof material | 210 | Design Team
 |  | Electrical part is washed | 350 | Alarm when vest is removed | 70 | Electrical Team
 | Circuit Malfunction | Exercise | 200 | Soldering circuit connection | 40 | Electrical Team
 | Out of power | Forgot to charge | 500 | Display shows battery condition | 100 | Electrical Team
Not Comfort-able | Does not fit | Different body sizes/types | 160 | Customizable / size variety | 80 | Design Team

## Slide 11: Team Skills
Skill Team Members | Electrics &Circuits | Programming | Handcrafting/Manufacturing Skills/ Sewing | Speaking & Organizing Speech | CAD & Sketching | Team Managing/ Leading | Mechanical Calculations
Madeleine Dwyer |  |  |  |  |  |  | 
Wen Fan |  |  |  |  |  |  | 
Ziye Hu |  |  |  |  |  |  | 
Yanting Liu |  |  |  |  |  |  | 
Baiting Luo |  |  |  |  |  |  | 
Adam Platek |  |  |  |  |  |  | 
Kangning Wang |  |  |  |  |  |  | 
Yuheng Zhou |  |  |  |  |  |  | 
Skill Proficiency
û: Weak Blank: Neutral ü: Strong

## Slide 12: Initial Final Design
Front View
Side View
Back View
300mm
References: 5, 19, 20, 21, 22, 28.

## Slide 13: Prototype Design
Three subsystems:
Inflation ( Arms)
Electrical
Vest Design

## Slide 14: Prototype Arm Design
300mm (11 inches)
300mm (11 inches)
300mm (11 inches)

## Slide 15: Prototype joint designs
CAD picture needed
 | Picture | Functionality
Ball & Socket |  | Freely adjusts contact angle with ground
Rotatory Damper |  | Opens freely Dampness prevents closing Opens to approximately 180 degrees
Pinned |  | Restricts left and right rotation

## Slide 16: Prototype Arm design Details
CAD picture needed
Bended Lower-rods | Welded Support | Aluminum Connection Rod
25˚
Aluminum Rod

## Slide 17: Prototype arm Assembly
Part | Manufacturing Steps | Equipment Used
Ball and Socket Joint | Buy joint Make connection | Drill press Lathe
Steel rods | Cut steel Drill holes Drill additional holes Bend steel Cut and weld gusset | Drill press Bending machine Acetylene/Oxygen torch MIG welding torch (low voltage)

## Slide 18: Prototype Arm assembly
Part | Manufacturing Steps | Equipment Used
Pinned Joints | Cut steel sheets Drill holes Round edges Bend steel Attach foam | Shear Steel cutting band saw Drill press Belt sander Metal bender
Base Plates | Cut steel Cut and attach foam pieces Drill holes through foam and steel Attach rubber and cut holes for screws | Steel cutting band saw Scissors Knife Drill press Super glue
Screws | Cut to size | Bench vice Titanium carbide wheel Belt sander Files
References: 1, 15, 16, 37 42, 44.

## Slide 19: Prototype Vest design
References: 46, 47.

## Slide 20: Prototype Vest assembly
Part | Manufacturing Steps | Equipment Used
Vest | Measure and cut Kydex plates Bend Kydex Sew pockets for Kydex Drill Kydex plates Laser cut vest holes Attach arms to Kydex Attach velcro | Band saw Heat gun Thread and Needles Hand drill Laser cutter Super glue
Trigger Hooks | Remove material to decrease hook curvature Attach to motor Cut and cauterize rope Sew onto vest | Belt sander Super glue Scissors Acetylene/Oxygen torch Needles and thread

## Slide 21: Prototype Electrical Design & Assembly
Stepper Motor
Buzzer
Switch
2560 Mega Microcontroller
3 axis gyro accelerometer
Battery

## Slide 22: Electrical Design – logic diagram
Notes: Pictures of circuit needed

## Slide 23: Sensor trigger data
 | Gyro Y(deg) | Accel X(g) | Accel Z(g)
Bend | 52.5 | 0.10 | 0.11
Walk | 10.0 | 0.10 | 0.06
Go upstairs | 17.5 | 0.28 | 0.01
Go Downstairs | 36.7 | 0.35 | 0.23
Fall | 90 | 0.30 | 0.43
Conclusion |  |  | 
Trigger data | 80 | 0.30 | 0.30
Horizontal Vertical Out of plane

## Slide 24: Prototype Design
Sketch of Prototype Design
Photo of Prototype Design

## Slide 25
 | Final design | Prototype
Number of arms | 6 arms | 2 arms
Max weight of users | 890 Newtons | 200 Newtons
Catch height | .91 meters | At least .3 meters
Color/Shape | Multiple color selections/Vest | Orange/Vest
Kydex plate | Stomach plate | No stomach plate
Sensor Placement | In vest pocket | On the belt
Mesh | Mesh inside the vest | Without mesh
Comparison: Prototype and initial final design

## Slide 26: Testing
Subsystem testing
System testing

## Slide 27: Subsystem Testing – design group
Design Group testing
  Based on Calculation
  Cannot do human body test
  Jumped on the curved Kydex
    No permanent deformation (without heat)
    Not broken
    Maintains shape
Punching a Kydex Plate

## Slide 28: Subsystem Testing – arm group
Arm testing
  Dummy falls down on carpet: 0.81s
  Dummy falls down on floor: 0.90s
  With arms on carpet: 1.88s
  With arms on floor: 1.82s
  Take-away: Consistently slows down a victim's fall
Arm Supporting the Dummy
Notes:   Consistently slows down a person’s falling by around 1s, which is critical
  0.78s/0.91/0.74
  0.96/0.80/0.96
  1.83/2.81/2.10
  2.03/1.73/1.69

## Slide 29: Subsystem Testing – electrical group
Circuit and sensor testing
  Walking
  Bending over
  Walking upstairs
  Walking downstairs
  Falling down
    Trigger Time: 0.56s
Testing Sensors by Walking Downstairs
Notes:     1.25 / 1.42 / 1.21

## Slide 30: Prototype Testing
Chart: Test Number
| 1 | 4 | 3 | 4 | 5 | 6
Sensor Trigger Time: 0.56s ± 0.3s | 0.58 | 0.41 | 0.81 | 0.68 | 0.44 | 0.53
Arm Deployment Time: 2.23s ± 1.77s | 1.9 | 3.8 | 4 | 2.65 | 1.75 | 1.71
Fall → Sensor Trigger → Arm Deployment

## Slide 31: Problems Encountered & solutions
Subsystems | Problems | Solutions
Electrical | Sensor and success rate： Loose pocket-bad readings Originally sensor worked intermittently. No area to place sensor(Kydex plates) Clip and hook kept falling. | Place sensor on a belt Super glue
Arm | Ball-and-socket joints did not bent to 45 degrees (ideal angle) Arm hinges loosened and dummy fell down quickly | Bend the steel rods Tighten hinges
Vest | Stomach Kydex plate did not fit - in way of sensor Velcro connecting motor to vest did not stick Zipper not simple enough for elderly | Remove stomach plate Change velcro type Use velcro to close vest

## Slide 32
Initial Final Design
Updated Final Design

## Slide 33: Production Ramp up
Use wedge lock joint
Make vest
Use ventilation foam
Increase friction of rubber coating bottom of base plates
Buy bulk materials
Each vest contains 4 legs
Increase availability of multiple colors and sizes
Increase motor speed and mount sensor inside vest
Use ball and socket joint with correct angle range (45 degrees)
Hire manufacturers
Use steel for ball and socket connection

## Slide 34: Review & Reflect
Prototype is not at realistic standards for a fall
  It will be in the future
Solvable prototype problems were corrected
Some prototype problems were not fixable
  Reasons:
    Time constraints
    Money constraints
Differences between the initial final design and the updated final design:
  Stomach plate removed
  Catch height is decreased

## Slide 35: Validation against customer needs - safety
Interpreted specifications | Final Design Requirement | Prototype Requirement | Prototype
Plate Location | stomach, shoulder, ribs, hips | stomach, ribs | Plate placement
Maximum Weight Limit | 890 Newtons | 200 Newtons | 200 Newtons
Sufficient Catch Height | .91 Meter | 0.3 meters | 0.3 meters
Arm deployment time | 1 second | 4 seconds | 1.3 seconds
Diameter of arm | 5.08 inches or less | 5.08 inches or less | 1.905 cm od 1.5875 cm id
References: 53

## Slide 36: Validation against customer needs – comfortable and ease of use
Interpreted specifications | Final Design Requirement | Prototype Requirement | Prototype
Suitable Size | standard unisex sizes (in.) Medium - Chest (38-40), Waist - (32-33) | One size/ medium | One size/ medium
Suitable Weight | ≤ 9 Kg | ≤ 9 Kg | 2.27kg
Number of Assembly Parts | ≤ 10 parts | ≤ 10 parts | 2
Time to assemble | ≤ 20 minutes | ≤ 20 minutes | ≤ 20 minutes
Time to reassemble | ≤ 5 minutes | ≤ 5 minutes | ≤ 5 minutes
Time to put on | ≤ 3 minutes | ≤ 3 minutes | ≤ 3minutes
Percent Shrinkage | assuming washable, < 5% | assuming washable, < 5% | 0%
Percent Dampness | 0% water reaching sensors | 100% | 100%
Temperature Moderation | At least 4 holes, >3 ventilation areas additional | Without mesh | Without mesh

## Slide 37: Validation against customer needs – Affordable & fashionable
Interpreted specifications | Final Design Requirement | Prototype Requirement | Prototype
Purchase cost | < $500 (subjective to change of cost analysis) | < $500 | $358.59
Color | Subjective | orange | orange
Shape | Subjective | vest | vest

## Slide 38: WHAT WE LEARNED
Engineering Design process
Communication& Teamwork
Machining techniques
Problem solving skills
[43]
[13]
[8]
Notes: Engineering process picture https://www.teachengineering.org/k12engineering/designprocess

## Slide 39: conclusion
To end: This is not getting better.
Cost of falls estimated to double by 2020.
Products on the market can’t stop falls.
Begin production ramp-up to manufacture larger quantities of the vest.
Primary Customer : patients and elderly people from nursing homes, hospitals, and eventually civilians once cost goes down.
References: 31.
Notes: Update gantt chart

## Slide 40: References
1. A. (n.d.). Material Selection Guide. Retrieved June 08, 2017, from http://www.applerubber.com/seal-design-guide/material-selection-guide/hydrogenated-nitrile.cfm ​
2. A. (n.d.). Retrieved June 08, 2017, from https://www.arduino.cc/en/Products/Compare
3. A. (n.d.). Suspa C16-08054 C1608054 20" Gas Prop, Quantity (2), Force 100 Lbs Per Prop, Force Per Set 200 Lbs, Camper Rear Window, Tonneau Cover Lift Supports, Window Lift Support, Made in USA: Automotive. Retrieved June 12, 2017, from https://www.amazon.com/Suspa-C16-08054-C1608054-Quantity-Supports/dp/B0041EBSX4/ref=sr_1_3?ie=UTF8&qid=1497298917&sr=8-3&keywords=gas%2Bspring​
4. Agency, V.( n.d.). PVC. Retrieved June 08, 2017, from http://www.pvc.org/en/p/pvcs-physical-properties​
5. Apparel, A. (n.d.). Size Chart: Men/Unisex Shirts. Retrieved June 12, 2017, from https://www.americanapparel.net/sizing/default.asp?chart=mu.shirts​
6. AT&T.(n.d.). AARP Recommendations. Retrieved June 08, 2017, from https://www.att.com/att/InnovationStore/images/products/everthere/docs/AARP.pdf​​
7. AT&T ForHealth EverThere alerts, guides emergency medical teams. (n.d.). Retrieved June 08, 2017, from https://www.slashgear.com/att-forhealth-everthere-alerts-guides-emergency-medical-teams-04307646/8.
8. Communication [Digital image]. (n.d.). Retrieved June 25, 2017, from http://blogs.oregonstate.edu/programevaluation/2017/04/17/communication/
9. C. (n.d.). Custom Advanced Connections. Retrieved June 08, 2017, from http://www.customadvanced.com/common-properties-of-rubber-elastomers.html​
10. D. (n.d.). Sensor Requirements for Human Fall Detection Systems. Retrieved June 08, 2017, from https://www.digikey.com/en/articles/techzone/2012/dec/sensor-requirements-for-human-fall-detection-systems​
11. Double Channel LM393 Tilt Slant Angle Sensor Module DC 3.3V-12V. (n.d.). Retrieved June 26, 2017, from https://www.amazon.com/Double-Channel-Sensor-Module-3-3V-12V/dp/B00HGAL2SQ

## Slide 41: References
12. E. (n.d.). Sports Mesh Fabric [Digital image]. Retrieved June 12, 2017
13. Engineering Design Process [Digital image]. (n.d.). Retrieved June 25, 2017, from https://www.teachengineering.org/k12engineering/designprocess.
14. Feynman, R., Gottlieb, M., Leighton, R. (2013). Feynman's Tips on Physics, A Problem-Solving Supplement to the Feynman Lectures on Physics. Basic Books.
15. Goodrich, R. (2013, October 01). Accelerometer vs. Gyroscope: What's the Difference? Retrieved June 08, 2017, from https://www.livescience.com/40103-accelerometer-vs-gyroscope.html
16. Group, S. (n.d.). Properties of aluminium. Retrieved June 08, 2017, from http://www.aluminiumdesign.net/why-aluminium/properties-of-aluminium/
17. Gyroscope. (2017, June 06). Retrieved June 08, 2017, from https://en.wikipedia.org/wiki/Gyroscope
18. H. (2017, March 28). Technology for fall prevention: Smart Slippers | HTS Therapy. Retrieved June 08, 2017, from https://www.htstherapy.com/technology-fall-prevention-smart-slippers/
19. Halls, D. (2017, June 10). Average weight chart and average weight for men by age. Retrieved June 14, 2017, from http://halls.md/average-weight-men/
20. Halls, D. (2017, June 13). Average weight for women, height weight charts. Retrieved June 14, 2017, from http://halls.md/average-weight-women/
21. Height Percentile Calculator, by Age or Country. (2016, May 06). Retrieved June 12, 2017, from https://tall.life/height-percentile-calculator-age-country/

## Slide 42: References
22.Hoekstra, R. (2016, September 15). My top five fabrics for clothing. Retrieved June 08, 2017, from http://www.made-by-rae.com/2013/07/my-top-five-fabrics-for-clothing/
23. I. (n.d.).Bijal Textiles [Digital image]. Retrieved June 12, 2017.
24. Kerkar, P., MD. (2017, May 26). Complete Displaced Fracture of Knee Joint [Digital image]. Retrieved June 25, 2017, from https://www.epainassist.com/joint-pain/knee-pain/knee-joint-fracture
25. KYDEX-T_Data [Advertisement]. (2011). Retrieved June 15, 2017, from https://www.professionalplastics.com/professionalplastics/KYDEX-T_Data.pdf
26. L. (n.d.). LIFE ALERT official website - I've fallen and I can't get up!®. Retrieved June 08, 2017, from http://www.lifealert.com/
27. M. (n.d.). Hip Fracture [Digital image]. Retrieved June 25, 2017, from http://www.massgeneral.org/conditions/condition.aspx?id=223
28. Master, M. A. (1960, February 13). TABLES OF AVERAGE WEIGHT AND HEIGHT OF AMERICANS AGED 65 TO 94 YEARS. Retrieved June 14, 2017, from http://jamanetwork.com/journals/jama/article-abstract/327589
29. MatWeb. (n.d.). Retrieved June 12, 2017, from http://www.matweb.com/search/QuickText.aspx
30. Medical Alert Devices with Fall Detection| Medical Alert Systems Medical Alert Advice. (2015, November 29). Retrieved June 08, 2017, from http://www.medicalalertadvice.com/fall-detection/
31. NCOA. (2017, May 31). Falls Prevention Facts. Retrieved June 08, 2017, from https://www.ncoa.org/news/resources-for-reporters/get-the-facts/falls-prevention-facts/

## Slide 43: References
32. Newsroom. Retrieved June 12, 2017, from https://www.census.gov/newsroom/facts-for-features/2016/cb16-ff08.html
33. O. (n.d.). OnCare smarter products. Better perfomance. Retrieved June 08, 2017, from http://www.oncaremedical.com/products/fallProducts.oncare?type=fall
34. O'brien, D. P., Luchette, F. A., Pereira, S. J., Lim, E., Seeskin, C. S., James, L., . . . Frame, S. B . (2002, October). Pelvic fracture in the elderly is associated with increased mortality. Retrieved June 08, 2017, from https://www.ncbi.nlm.nih.gov/pubmed/12407356
35. Office, A. T. (2008, July 16). Balance problems? Step into the iShoe. Retrieved June 08, 2017, from http://news.mit.edu/2008/i-shoe-0716
36. Plastics, I. (n.d.). KYDEX PRE-CUT 2X4 FT. BUNDLES [Digital image]. Retrieved June 12, 2017.
37. Polymer database.com, C. %. (n.d.). Polymer Properties Database. Retrieved June 08, 2017, from http://polymerdatabase.com/Elastomers/HNBR.html
38. Preece, J. (2017, May 03). The Best Fall Detection Sensors | Top Ten Reviews. Retrieved June 08, 2017, from http://www.toptenreviews.come/health/senior-care/best-fall-detection-sensors/
39. Proxy, I. S. (2015, April 10). Physical Properties of Rubber – a Buyer and Designer's Guide . Retrieved June 08, 2017, from http://www.azom.com/article.aspx?ArticleID=11914
40. Rubber Materials & Elastomer Compound Information. (n.d.). Retrieved June 08, 2017, from http://www.columbiaerd.com/materials.html
41. S. (2012, August 27). 10 Shocking Statistics About Elderly Falls. Retrieved June 08, 2017, from http://shellpoint.org/blog/2012/08/13/10-shocking-statistics-about-elderly-falls/
42. S. (n.d.). Gyroscope. Retrieved June 08, 2017, from https://learn.sparkfun.com/tutorials/gyroscope

## Slide 44: REFERENCES
43. Spacial problem solving approach [Digital image]. (n.d.). Retrieved June 25, 2017, from https://learn.arcgis.com/en/related-concepts/spatial-problem-solving-approach.htm
44. Standard Drill Sizes - Inches. (n.d.). Retrieved June 12, 2017, from http://www.gearhob.com/eng/design/drill_eng.htm
45. T. (n.d.). MPU-6050 | TDK. Retrieved June 08, 2017, from https://www.invensense.com/products/motion-tracking/6-axis/mpu-6050/
46. Toolbox, E. (n.d.). Material Properties. Retrieved June 08, 2017, from http://www.engineeringtoolbox.com/material-properties-t_24.html
47. Toolbox, E. (n.d.). Polymers - Physical Properties. Retrieved June 08, 2017, from http://www.engineeringtoolbox.com/polymer-properties-d_1222.html
48. Toolbox, E. (n.d.). Thermoplastics - Physical Properties. Retrieved June 08, 2017, from http://www.engineeringtoolbox.com/physical-properties-thermoplastics-d_808.html
49. US Census Bureau Public Information Office. (2016, May 19). Newsroom Archive. Retrieved June 12, 2017, from https://www.census.gov/newsroom/releases/archives/miscellaneous/cb12-134.html
50. Uxcell® 15Pcs DC 5V 85dB Industrial Active Electronic Alarm Buzzer: Automotive. (n.d.). Retrieved June 26, 2017, from https://www.amazon.com/uxcell-Industrial-Active-Electronic-Buzzer/dp/B016FCBBT0/ref=sr_1_4?ie=UTF8&qid=1498412942&sr=8-4&keywords=buzzer
51. V. (n.d.). Technical illustration of a three-layer fabric. [Digital image]. Retrieved June 12, 2017
52. W. (n.d.). Falls. Retrieved June 08, 2017, from http://www.who.int/mediacentre/factsheets/fs344/en/
53. Wentworth, K. (2012, August 21). How Much Force Can Our Bones Handle Before They Break. Retrieved June 12, 2017, from http://ezinearticles.com/?How-Much-Force-Can-Our-Bones-Handle-Before-They-Break&id=7242657

## Slide 45: Thank you!

## Slide 46: Questions?

## Slide 47: Appendix A :Product Subsystems
Notes: No reference

## Slide 48: Appendix B : Functional Subsystems
Notes: No reference

## Slide 49: Appendix C : Gantt Chart
Notes: No reference

## Slide 50: Appendix d– Circuit Diagram

## Slide 51: Appendix e - Calculations for Arms
Stresses in Arm:
Stresses in Joints:
Falling Force:
E (Young's Modulus) = 45 GPa, G (Shear Modulus) = 52 GPa
References: 14, 29.